## Slide 1: Town of Irvington Stakeholder Meeting Results & Discussion
Prepared by EPR, P.C. for the Town of Irvington
March 23, 2023

## Slide 2: Public Sewer System

## Slide 3: Town Efforts To-Date: Sewer Advisory Panel, March 2022
Potential Scenarios:
A. Conventional and Alternative Onsite Sewer Systems with clustered Decentralized Systems
  EPA endorses these systems as long-term treatment alternatives
  Residents continue to operate and maintain their systems
  New and replacement systems installed as needed
    Conventional system replacement $8,000
    Drain field replacement: $4,500
    AOSS replacement: $30,000
B. Town Center collection system with treatment by Kilmarnock
  1.4-mile low pressure force main down KC drive and out RT 200 to town limit with 1.8-mile pumping station to Kilmarnock connection
  Assumes 20 resident connections and ICN/King Carter Holdings and Vineyard Meadows connections by them
  Kilmarnock connection fee estimate $10,000 and home connection estimate $2,000
  Best Guess Capital cost: $2.4 million, range $2.3 to $3.2 million
C. Complete Town collection system with treatment by Kilmarnock
  Estimate 8 miles of low-pressure force main through Town with 1.8 miles with pumping station to Kilmarnock connection
  380 potential connections with assumed 266 actual connections
  Kilmarnock connection fee $10,000 and home connection $2,000
  Best Guess Capital cost: $7.5 million, range $7.2 to $9.8 million
Notes: Council has authorized a feasibility study – also refer people to the presentation (on the town website)

## Slide 4: Existing Municipal Sewer Systems in the Region

## Slide 5: 2022 Community Survey Results Opinions on Sewer Services (check all that apply)
Chart: 
| The Town does not need to invest in a public sewer system at this time | I would be willing to pay a one-time cost (estimated at a minimum of $12,000) to connect to sewer service [there would be no requirement to connect] | I have experienced difficulties with my septic system that required repair or service in the last 5 years | Wet or rainy weather sometimes causes issues with my septic system | No response
 | 181 | 149 | 73 | 46 | 35
Note: Percentages of total responses. Respondents could select multiple options
50%
Notes: On “Opinions on Sewer Services”:
7 people selected both “I have experienced difficulties with my septic system that required repair…” and “The Town does not need to invest in a public sewer at this time”
1 person selected both “Wet or rainy weather sometimes causes issues with my septic system” and “The Town does not need to invest in a public sewer at this time”
No one selected “I have experienced difficulties…”, “Wet or rainy weather…”, and “The Town does not need to invest…”

## Slide 6: Public Sewer: 2023 Stakeholder Meeting Responses
Chart: 
A need for more information about cost, feasibility, etc. before forming an opinion
Support for a limited option that serves King Carter Dr. and the Tides Inn
Support for a sewer system that serves the entire town, but where connection would be voluntary
Concern that a sewer system would attract unwanted growth
Some opposition to a sewer system in general
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
8 | 6 | 9 | 4 | 2

## Slide 7: Waterfront Public Access

## Slide 8: Existing Waterfront Access in the Region

## Slide 9: Planned Waterfront Access in the Region
Lancaster County has been awarded a $150,000 planning grant from the Virginia Outdoors Foundation to help develop the new Carter Cove County Park in Weems. The grant, pursued by a citizen board appointed to help with public access, is a major step in the goal of getting better public access to the waters surrounding Lancaster County. The five-acre parcel for the new park was acquired by the county earlier this year. Proposed amenities include:
A kayak/canoe launch,
Fishing pier,
Picnic shelter, and
A boat ramp with courtesy dock.
4.5 miles (8 minutes) from Irvington

## Slide 10: Existing Private Waterfront Access in Irvington
Chart: ~60% of residences have waterfront access ~38% of residences do not have waterfront access ~2% have access to the creek
| Waterfront Access | No Waterfront Access | Creek Access
Number | 211 | 135 | 12
Note: this is an estimate based on analysis of aerial imagery.

## Slide 11: 2022 Community Survey Results Opinions on the waterfront and public water access (check all that apply)
Note: Percentages of total responses. Respondents could select multiple options
Chart: 
| I see no need to acquire waterfront property beyond what is currently available | I would like for the Town to acquire waterfront property for boat/kayak access | I would like for the Town to acquire waterfront property for a park or gathering space | I would like for the Town to acquire waterfront property for a fishing dock | I would like for the Town to acquire waterfront property for swimming | No response
 | 175 | 154 | 141 | 72 | 64 | 12
50%
Notes:   112 people selected both “I would like for the Town to acquire waterfront property for boat/kayak access” and “I would like for the Town to acquire waterfront property for a park or gathering space”

## Slide 12: Waterfront Access: 2023 Stakeholder Meeting Responses
The Gaskins property is sufficient. If it were to change hands, the Town should pursue a right of first refusal.
It would be nice to have some amenities like a fishing pier, small waterfront park, a restaurant with waterfront access, a place to put small craft in the water, etc., but it’s not a priority
There’s enough public water access in the area already
Public water access in town would attract too many people and unwanted traffic
A need for more information about cost, feasibility, purpose, etc. before forming a strong opinion either way
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
3 | 9 | 9 | 4 | 3

## Slide 13: Future Residential Development

## Slide 14: Existing Housing & Developable Land
According to the 2020 Census, there are currently a total of ~368 housing units in Irvington:
  246 units are occupied full-time
  122 units are “vacant” or occupied seasonally

## Slide 15: Map of Developed, Undeveloped, & Underdeveloped Land
Note: this is an estimate based on analysis of aerial imagery.

## Slide 16: Estimated Developable Land Acreage
Chart: ~524 acres are developed (at least one building on property) ~353 acres are undeveloped (no buildings on property) ~50 acres are “underdeveloped” (high land-to-building ratio)
| Undeveloped Parcels | Underdeveloped Parcels | Developed Parcels
Sales | 186 | 4 | 485
Note: this is an estimate based on analysis of aerial imagery.

## Slide 17: 2022 Community Survey Results Opinions on New Growth (check all that apply)
Chart: 
| I would support new businesses and restaurants in Town that fit with Irvington’s character | I would support new homes in Town that fit with Irvington’s character | I would prefer the town remain as it is, with limited additional residential and commercial development | I am unsure about increased residential or business development in Town | No response
 | 231 | 206 | 132 | 22 | 2
Note: Percentages of total responses. Respondents could select multiple options

## Slide 18: 2022 Community Survey Results Opinions on Housing Types (check all that apply)
Chart: 
| I would prefer to keep our town’s housing types as they are now | I would like to see more smaller/starter/retirement homes that match the town’s character | I would like to see more apartments in Town | I would like to see more duplexes in Town | No response
 | 244 | 134 | 24 | 24 | 7
Note: Percentages of total responses. Respondents could select multiple options
Notes: Will

## Slide 19: Future Residential Development: 2023 Stakeholder Meeting Responses
Preservation of the Town’s existing character
Acceptance of additional single-family residential development in line with existing zoning that happens without any specific intervention by the Town
Opposition to multifamily housing
A need for more smaller, less expensive single-family housing options for young families and those looking to age in place
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
4 | 6 | 17 | 0 | 2

## Slide 20: Other Topics

## Slide 21: Meals Taxes in the Region
Tappahannock: 6%
Kilmarnock: 5%
Urbanna: 5%
Warsaw: 5%
White Stone: 2.5%
Westmoreland County: 5%
Middlesex County: 4%
Mathews County: 4%
Gloucester County: 4%
Montross: No meals tax
Reedville: No meals tax
Essex County: No county-wide meals tax
Lancaster County: No county-wide meals tax
Richmond County: No county-wide meals tax
Northumberland County: No county-wide meals tax

## Slide 22: Meals Taxes in the Region

## Slide 23: Meals Taxes: 2023 Stakeholder Meeting Responses
A need for more information and clarity on what the meals tax would be used for before forming a strong opinion either way
Conditional support for a meals tax with a defined purpose and end date
Opposition to any additional taxes and a sense that the Town has enough money
Support for a meals tax around 2.5% that goes directly towards a sewer system
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
0 | 9 | 8 | 2 | 5

## Slide 24: Town Commons Improvements: 2023 Stakeholder Meeting Responses
Chart: 
General support for minor, inexpensive improvements to landscaping, beautification, etc.
Support for public restrooms, specifically mobile ones that are less costly and easier to install/remove
Support for resurfacing the tennis courts
Support for refurbishing the playgrounds
Satisfaction with things the way they are
Opposition to spending a lot of money on improving the Commons
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
7 | 12 | 4 | 1 | 3

## Slide 25: Sidewalk Improvements: 2023 Stakeholder Meeting Responses
General support for repairing existing sidewalks
Some support for extending the sidewalk to the other side of Irvington Rd.
Some support for filling in gaps where there is no sidewalk
General opposition to installing sidewalks in West Irvington due to ditches, encroachment on private property
Some support for widening sidewalks where feasible
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
7 | 14 | 6 | 0 | 0

## Slide 26: Traffic Calming: 2023 Stakeholder Meeting Responses
All participants were in favor of some form of traffic calming in Town
Some participants were in favor of enhanced enforcement, speed traps, a police officer on duty, etc.
Some support for speed bumps, bump-outs
Some support for traffic circles and other efforts that could also enhance beautification
Some support for enhanced golf cart access throughout town as well as improvements to crossings and parking
Support | Conditionally Support | Neutral | Conditionally Oppose | Oppose
23 | 1 | 0 | 0 | 0